## Slide 1: BA 291 – operational management and control
By Aj. Parichat Jantori

## Slide 2: Operational Management
Operations Management: The development and administration of the activities involved in transforming resources into goods and services
Operations managers oversee transformation process and the planning and designing of operation system, managing logistic, quality and productivity

## Slide 3: Transformation Process
Notes: Ask: transformation process in service industry
Airlines input: employees, time , money, equipment
Process: booking flight, flying airplane, maintaining the equipment, training the crew
Output: flying passenger to the destination
More examples: p. 267

## Slide 4: Manufacturing vs. Service Providers
  Produce tangible or intangible goods
  Most goods are manufactured prior to purchase, most services are performed after purchase
  Manufacturing can occur in an isolated environment, away form customers. Customer contact is significant component to most services.
  Uniformity of inputs – automated or customize
  Uniformity of outputs
  Labor required – service is more labor intensive
  Measurement of productivity – service industry has great variation

## Slide 5: Objectives of operational management
Increase output
Increase efficiency (productivity = output/ input)
Lower cost
Increase quality of products and services
Factors influenced productivities
Labor (quality of labor)
Capital fund
Management
Notes: Labor (quality of labor) (10%)
Capital fund (38%)
Management (52%)

## Slide 6: Planning and designing operation systems
Planning the products
  What consumers want
  Design product to satisfy the want
  Marketing research (focus group, survey, observation)
  Types and quantities of raw materials
  Skills & quantity of labor
  Processes for transformation to outputs
  Cost and time intensive

## Slide 7: Planning and designing operation systems
Designing the operation processes
Standardization – the making of identical interchangeable components or products.
Example: Televisions, Ballpoint pens, Tortilla chips
Advantages:

## Slide 8: Modular design

## Slide 9: Modular design
creation of an item in self-contained units that can be combined or interchanged to create different products
  Personal computers -- CPU’s, motherboards, monitors

## Slide 10: Modular design
Prefabrication
Notes: http://www.smilingprefab.com/home_th.html

## Slide 11: Modular design
Advantages:
Less labor demand – cost reduction
Reducing production time (some components can bought from suppliers)
Allows products to be repaired quickly

## Slide 12: Customization
making products to meet a particular customer’s needs or wants
One-size doesn’t fit all
Produce unique product to serve individual’s needs

## Slide 13: Mass customization
Mass customization calls for a customer-center orientation in production and delivery processes, requiring the company to collaborate with individual customers to design each one's desired product or service, which is then constructed from a base of pre-engineered modules that can be assembled in myriad ways.
Using modular design, flexible production layout
Dell computer
Automobile industry
Notes: http://www.dell.com/us/p/laptops
http://www.mercedes-benz.de/content/germany/mpc/mpc_germany_website/de/home_mpc/passengercars/home/new_cars/configurator_showroom.flash.html

## Slide 14: Planning and designing operation systems
Planning capacity
Capacity – The maximum load that an organizational unit can carry or operate
Capacity utilization – the degree to which current scale of operation is actually being used.
Capacity can be increased through introducing new techniques, equipment and materials, increasing the number of workers or machines, increasing the number of shifts, or acquiring additional production facilities
Notes: If the operating rate is high, this is called "overcapacity", while if the operating rate is low, a situation of "excess capacity" or "surplus capacity" exists

## Slide 15: Planning and designing operation systems
Planning facilities
Planning facility location
Facility location is the process of identifying the best geographic location for a service or production facility
Choosing country – region – exactly place

## Slide 16: Facility location
Making Location Decisions
  Step 1: Identify dominant location factors
  Step 2: Develop location alternatives
  Step 3: Evaluate locations alternatives

## Slide 17: Evaluate Facility location
- Cost comparison (establishing cost, yearly cost)
- Factor Rating

## Slide 18: Facility location
Break-even Analysis
Clean-Clothes Cleaners is considering four possible sites for its new operation. They expect to clean 10,000 garments. The table and graph below are used for the analysis.
 | fix cost | var cost | var cost | total
Location A | 350000 | 5 | 50000 | 400000
Location B | 170000 | 25 | 250000 | 420000
Location D | 100000 | 40 | 400000 | 500000
Location E | 250000 | 20 | 200000 | 450000
Notes: From the graph you can see that the two lowest cost intersections occur between C & B (4667 units) and B & A (9000 units)
The best alternative up to 4667 units is C, between 4667 and 9000 units the best is B, and above 9000 units the best site is A

## Slide 19: Planning and designing operation systems
Planning facility layout
Fixed-Position Layout--Project organization
  All resources needed for a product are brought to a central location.

## Slide 20: Planning facility layout
Process Layout--Intermittent organization
  Layout is organized into departments that group related processes.

## Slide 21: Planning facility layout
Product Layout--Continuous manufacturing organization
  Production is broken down into relatively simple tasks assigned to workers positioned along a line.
Notes: http://www.youtube.com/watch?v=rXG1a6pU5K4&feature=related
http://www.youtube.com/watch?v=La73Oy9ZGVw&feature=related
http://www.youtube.com/watch?v=2aNn1nRD15c

## Slide 22: Managing the Supply Chain
Connecting and integrating all parties or members of the distribution system in order to satisfy customers
Include all the activities involved in obtaining and managing raw materials and component parts, managing finished products, packaging them and getting them to customers.

## Slide 23: Purchasing and Inventory control
Purchasing or procurement is the buying of all the materials needed by the organization. The aim is to obtain items of the desired quality in the right quantities at the lowest possible cost.
Inventory control is the process of determining how many supplies and goods are needed and keeping track of quantities on hand, where each item is and who is responsible for it. Aim of inventory control is to determine the proper inventory level for each item.
Notes: Inventory: all raw materials, components, completed or partially completed products, and pieces of equipment a firm uses

## Slide 24: The important of inventory management
Inventory in the warehouse costs money
Money not tied up in inventory can be used in other productive ventures
Products lose value every day

## Slide 25: Economic Order Quantity
EOQ is a model that identifies the optimum number of items in order to minimize the costs for managing them (ordering, storing)
Order in a large quantity
Economy of scales
Bulk discount
Order in a large quantity
High storage cost

## Slide 26: Economic Order Quantity
Company XYZ sells television to customers. It buys the TVs directly from manufacturer at price 1000 bath each. Every oder will cost company XYZ 20 bath. Based on the statistic, customers demand for TV per year is 8000 units. The storage cost is 2 bath per units.
Ordered quantity | Frequence of order | Cost of order (OC) | Averaged storaged number | Storage cost | Total Cost
100 | 80.00 | 1600 | 50 | 100 | 1700
200 | 40.00 | 800 | 100 | 200 | 1000
300 | 26.67 | 533 | 150 | 300 | 833
400 | 20.00 | 400 | 200 | 400 | 800
500 | 16.00 | 320 | 250 | 500 | 820
600 | 13.33 | 267 | 300 | 600 | 867
700 | 11.43 | 229 | 350 | 700 | 929
800 | 10.00 | 200 | 400 | 800 | 1000
900 | 8.89 | 178 | 450 | 900 | 1078
1000 | 8.00 | 160 | 500 | 1000 | 1160

## Slide 27: Economic Order Quantity
Chart: 
| 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
CC | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
OC | 1600 | 800 | 533.3333 | 400 | 320 | 266.6667 | 228.5714 | 200 | 177.7778 | 160
Total Cost | 1700 | 1000 | 833.3333 | 800 | 820 | 866.6667 | 928.5714 | 1000 | 1077.7778 | 1160

## Slide 28: Just-in-time inventory management
An inventory control system that schedules materials to arrive precisely when they are needed on a production line.
Reducing raw material inventories: Suppliers deliver materials only at the exact moment need
Work-in process inventories are kept to minimum because goods are produced only as needed to service the next stage of production.
Finished good inventories are minimized by matching them exactly to sales demand.
Stockless system, zero inventory system
Notes: JIT allows manufacturers to purchase and receive components just before they're needed on the assembly line, thus relieving manufacturers of the cost and burden of housing and managing idle parts
Labor strikes, stock outs, and port lockouts can quickly disrupt an entire supply chain while JIT processes are in place. "Adhering to the just-in-time concept can be expensive in times of emergency such as at ports" (Greenburg, 2002). When a ship arriving from Asia full of supplies cannot make it to shore, the company using JIT generally has very little inventory to compensate for the emergency. This lack of inventory is exactly what makes JIT so great to companies in reducing costs, yet making it risky as well by in some cases not having enough buffer inventories to react and keep the supply chain moving. Every year markets experience seasonal demand fluctuations as well as fluctuations due to demand from disasters or other unforeseen events. "Just-in-time delivery leaves retailers and manufacturers with little inventory as the holiday season approaches" (Greenberg, 2002). Relying solely on JIT systems would leave supply chains in shock due to the overwhelming seasonal market demand at different times of the year for seasonal products. Not all products should be produced with JIT systems in place. Custom made items will not work well with JIT as JIT systems respond best to mass produced and highly automated production items.

## Slide 29: Just-in-time inventory management
Strenghts | Weakness

## Slide 30: Outsourcing
Outsourcing has become a component of supply chain management in operation
Outsourcing refers to the contracting of manufacturing or other tasks to independent companies

## Slide 31: Outsourcing
Make when:
Cost considerations (less expensive to make the part)
Desire to integrate plant operations
Productive use of excess plant capacity to help absorb fixed overhead (using existing idle capacity)
Need to exert direct control over production and/or quality
Better quality control
Design secrecy is required to protect proprietary technology
Unreliable suppliers
No competent suppliers
Desire to maintain a stable workforce (in periods of declining sales)
Quantity too small to interest a supplier
Control of lead time, transportation, and warehousing costs
Greater assurance of continual supply
Provision of a second source
Political, social or environmental reasons (union pressure)

## Slide 32: Outsourcing
Buy when:
Lack of expertise
Suppliers' research and specialized know-how exceeds that of the buyer
cost considerations (less expensive to buy the item)
Small-volume requirements
Limited production facilities or insufficient capacity
Desire to maintain a multiple-source policy
Indirect managerial control considerations
Procurement and inventory considerations
Brand preference
Item not essential to the firm's strategy
Notes: http://www.referenceforbusiness.com/management/Log-Mar/Make-or-Buy-Decisions.html

## Slide 33: Quality Management
Quality is the degree to which a good or service meets the demands and requirements of customers.
Quality control is the processes an organization uses to maintain its established quality standard.

## Slide 34: Quality Management
„Quality is free; by contrast, not having high quality goods and services can be very expensive, especially in term of dissatisfied customers“
(Philip B. Crosby, 1979, P. 9)
Notes: Quality – value creation, differentiation

## Slide 35: Total quality management
Total Quality Management (TQM) – philosophy that uniform commitment to quality will promote a culture that meets customers’ perceptions of quality.

## Slide 36: ISO
ISO 9000 – International Organization for Standardization (ISO) system of quality management standards designed to ensure the customer’s quality standards are met.